## Slide 1
6th November 2017 (21:00 GMT)
H72
B4C1 (EUR)
B4C2 (U49)
B4C3 (CAL)
B4C4 (CAN)
B4C5 (AUS)
B4C7 (THA)
B4C8 (TWN)
B8M1(EUR)
B1M1(AUS)
2018

## Slide 2
* Local release dates are set based on each local marketing strategy.
* Any information for each model code can’t be disclosed by above mentioned local release date.

## Slide 3
4
5
8
18

## Slide 4
“Acquiring The newer MT-ness”
EUR,U49,CAL,CAN, AUS
B4C1/8/B1M1/B8M1
…DPBMC/MNM3/MDNM6
B4C2/3/4/7
…DPBMC/MNM3/BWP1
B4C5
…MDNM6
DPBMC:DEEP PURPOSE BLUE METALLIC C
MNM3:MAT GRAY METALLIC 3
MDNM6:MAT DARK GRAY METALLIC 6
BWP1:BLUISH WHITE PEARL 1
New exterior styling: more attractive look and greater pride of ownership
・All-new body panels and plastics
・New head light and styling to more closely resemble bigger MT models
・Detail changes throughout
・Same as current EG character
Revised chassis and seat: better performance in more sporty riding
・New front fork specs
・New rear shock with rebound adjuster
・More comfortable seat design
・Same as current digital instrument cluster and easy-to-operate switches

## Slide 5
CONFIDENTIAL
FEATURE MAP : BODY
Model : H72
Newly designed winglet and exterior covers
Newly designed taillight
Newly designed rear shock absorber
Handlebar with new color paint
(silver  black paint)
Newly designed seat
Brake pedal shape is changed
Newly designed headlight and winglets
Front suspension settings is changed
Newly designed front fender
Front flasher location is changed
Newly designed scoop air and exterior covers
Running weight: 183kg (Compared to 1WS: 182kg)
Weight ratio: Front 49.2%(90kg), Rear 50.8%(93kg)
Newly designed radiator cover

## Slide 6
Model : H72
H
CONFIDENTIAL
DIMENSION MAP
G
B
F
A
E
D
ITEM |  | H72 | 1WS
A | Overall length | 2085 mm | 
B | Overall width | 745 mm | 
C | Overall height | 1090 mm | 
D | Seat height | 805mm | 
E | Wheel base | 1400 mm | 
F | Minimum ground clearance | 140 mm | 
G | Caster angle | 24.5 degrees | 
H | Trail | 90 mm | 
C

## Slide 7
Grip point
Foot point
Hip point
X
Y
Z
X: 660mm
Y: 860mm
Z: 485mm
Riding position is same as 1WS

## Slide 8
Newly designed exterior covers
Color of handlebars, gearshift rods, brackets and more changed from silver to black
The number of covers and panels were reduced to refresh the model’s look
Exterior parts
Attractive appearance
H72
1WS
New exterior design
・The exterior body panel and covers were all redesigned for higher quality

## Slide 9
Newly designed exterior covers , body panel and newly designed scoop air are adopted
Fuel tank covers
Attractive appearance
1WS
H72
Scoop air
Side cover
Inner panel
Fuel tank
New exterior design
・The exterior covers were all redesigned for higher quality

## Slide 10
Newly designed exterior covers and winglet are adopted
Rear cowl
Attractive appearance
1WS
H72
Side cover
Winglet
Taillight cover
Rear fender cover
New exterior design
・The exterior covers were all redesigned for higher quality

## Slide 11
Newly designed radiator cover is adopted
Front flasher location is changed from headlight cover to radiator cover
Radiator cover
Attractive appearance
Front Flasher
Radiator
Radiator cover
New exterior design
・The exterior covers were all redesigned for higher quality

## Slide 12
Newly designed front fender is adopted
Consist of front fender is changed from 3-pieces to 1-piece
Newly designed front fender
Attractive appearance
Side view
Top view
Top view
Side view
1WS
H72
3-pieces
1-piece
New exterior design
・The exterior covers were all redesigned for higher quality

## Slide 13
Shape is changed
New color paint (silver  black paint)
Brake pedal
Attractive appearance
1WS
H72
194 mm
40 mm
62 mm
62 mm
40 mm
194 mm
222 mm
222 mm
Shape change

## Slide 14
Newly designed seat is adopted
Cushion volume is increased
Flat sitting portion for rider is increased by 30%
Leather spec is not changed
Seats
Optimized cushioning shape
Side view
Top view
・The front end of the seat was extended 10 mm forward onto the fuel tank area to bring more freedom to the riding position
- H72
- 1WS
1WS
H72
Optimize for wide range of riding scenes
1WS
H72

## Slide 15
Spring and damper specification are changed
Shape is same as 1WS
Manufacturer is same as 1WS: KYB
Front fork
Good handling
Optimize for wide range of riding scenes
Items | H72 | 1WS
Stroke | 130 mm | 
Spring rate | 18 N/mm | 17 N/mm
Tension damping force @ 0.3m/s | 180 N | 155 N
Compression damping force @ 1.0m/s | 130 N | 
Oil quantity | 405 cm3 | 403 cm3
Oil level | 160 cm3 | 162 cm3
・Give riders a greater degree of adjustability and to better accommodate a wide variety of uses and rider skill levels

## Slide 16
Newly designed rear shock absorber is adopted
Spring and damper specification are changed
Rebound damping adjuster is adopted
Manufacturer is same as 1WS: KYB
Rear shock absorber
Good handling
Fun riding for wide range of riding scenes
Rebound damping adjuster
Items | H72 | 1WS
Spring rate | 120 N/mm | 107.8 N/mm
Tension damping force @ 0.3 m/s | 2200 N | 1730 N
Tension damping force @ 0.1 m/s | 765 N | 825 N
Compression damping force @ 0.3 m/s | 670 N | 480 N
Compression damping force @ 0.1 m/s | 350 N | 255 N
Rebound damping setting | Initial : One turn and half back from fully tightened position | -
Initial preload setting | 9 steps Initial: 3rd step | 
Spring preload adjuster
・The rear shock gains the same rebound adjustability as the current MT-09 and easier preload adjustability.
1WS
H72

## Slide 17
Sport type tire is adopted. Manufacture: Michelin, Bridgestone
Michelin-spec version uses Pilot Road 4s
Bridgestone tire spec is unchanged
Tires
Good handling
FRONT | PILOT ROAD 4 TL 120/70ZR17 M/C(58W)
REAR | PILOT ROAD 4 TL 180/55ZR17 M/C(73W)
For good handling
1WS
H72
FRONT | PILOT ROAD 3 TL 120/70ZR17 M/C(58W)
REAR | PILOT ROAD 3A TL 180/55ZR17 M/C(73W)
Tire air pressure
Front: 225 kpa / Rear: 250 kpa

## Slide 18
BU2 base wire harness is adopted
Wire harness specification is changed to correspond to change of front flasher location
Electrical parts location
To correspond to change of front flasher location
Optimized compact location
Front flasher
Stator
Rear wheel sensor
Instrument panel
Starting motor
Front wheel sensor
Rectifier regulator
HU
Ignition coil
Battery
ECU
Rear flasher
Main switch

## Slide 19
Newly designed headlight is adopted
Newly designed covers and winglet are adopted
Auxiliary light location is changed
Headlight
Attractive appearance
Rear view
Side view
Front view
Side view
Headlight lens
Winglet
Headlight cover
Front view
Rear view
New exterior design
1WS
H72
Auxiliary light
Auxiliary light

## Slide 20
Newly designed LED taillight is adopted
External lens shape is changed
Taillight
Attractive appearance
Rear view
Top view
Rear view
Top view
Stop light turn on all leds light
Taillight turn on 6 leds of each side light
New exterior design
1WS
H72